## Slide 1: Lecture 11 General Purpose GPU computing
GPCPU

## Slide 2: Contents
GPUs: overview and history (already done)
GPU Architecture (already done)
CPU/GPU Interaction
Applications
Discussion
Summary

## Slide 3: CUDA
In November 2006 NVIDIA released the first Direct X 10 GPU, the GeForce 8800 GTX.
This was the first GPU to be built with NVIDIA’s CUDA architecture

## Slide 4: CUDA
The CUDA architecture added several new components designed strictly for GPU computing
  every ALU on the chip could be used by a program for general-purpose computations.
  ALUs implemented by using an IEEE standard
  single precision floating point arithmetic included instruction sets
  suitable for general computation

## Slide 5: GPU vs CPU performance (2001-2014)
http://michaelgalloy.com/wp-content/uploads/2013/06/cpu-vs-gpu.png

## Slide 6: OpenCL
“The open standard for parallel programming of heterogeneous systems”
  Initially targeted for graphics cards, but also CPUs, DSPs, and more…
    e.g. Allows parallel kernels to be run on CPU with SIMD instructions, or on GPU

## Slide 7: OpenCL
Alternative to CUDA – non-proprietary
  First released Nov. 2008
  Managed by Kronos Group industry standardisation forum
  https://www.khronos.org/opencl/

## Slide 8: CPU/GPU Interaction

## Slide 9: Using CPU and GPU
GPUs are designed as numeric computing engines
Program
Sequential part
Parallel part
CPU
GPU

## Slide 10: Using CPU and GPU
Won’t perform well on some tasks on which CPUs are designed to perform well
  Most applications will use both CPUs and GPUs
    CPU - sequential parts, management, I/O
    GPUs - numerically intensive (parallel)
    parts
Program
Sequential part
Parallel part
CPU
GPU

## Slide 11: CPU/GPU interaction
The CPU is the Host, and runs the main program and any sequential code
The GPU is a compute device, which is attached to and managed by the host

## Slide 12: CPU/GPU interaction
The basic unit of parallel execution is a kernel, roughly a C/C++ function
  The host compiles and sends kernel(s) to the GPU
  The GPU can execute many copies of a kernel at once, each on different data (work item)
  The GPU schedule work items – like small threads – on the available SPUs (Stream Processing Unit)

## Slide 13: CPU/GPU Interaction
The CPU and GPU work in parallel with each other

## Slide 14: CPU/GPU Interaction
They communicate asynchronously via command queues or buffers
  Care is needed to maintain synchronization
  If command buffer becomes empty the GPU sits idle waiting for new input (CPU limited)
  If the command buffer becomes full CPU sits idle waiting for GPU to consume data (GPU limited)
CPU writes commands
GPU reads commands
Pending GPU commands

## Slide 15: Synchronisation issues between a CPU and GPU
Two approaches to dealing with synchronisation issues:
Inlining data: Inline all data to the command buffer, but bad for performance
Renaming data: Allocate a new data block and initialise

## Slide 16: Memory
In general:
  Kernels do not (often cannot) access main memory
  Each kernel works with
    its own private memory
    plus some local memory (shared by a group of work items)
  The application must move data explicitly between host, device, global and local memory
Note: compared to multi-core, a more complicated application model, but no single memory bottleneck

## Slide 17: Applications

## Slide 18: GPGPU Applications
Used in game physics calculations (physical effects like debris, smoke, fire, fluids)
Have also been used to accelerate non-graphical applications in computational biology, cryptography and other fields,
e.g.
  Medical imaging
  Computational fluid dynamics
  Environmental science

## Slide 19: Applications
Molecular Biology Research Simulations:
The size of the biological system that can be simulated

## Slide 20: Applications
A vast quantity of processing is necessary for HDTV.
It is a very parallel process as are 3D imaging and visualisation

## Slide 21: Applications
With increased computing speed games can be based on dynamic simulation rather than prearranged scenes.
Realistic modelling and simulation of physical effects - demand large amounts of computing power

## Slide 22: Discussion

## Slide 23: GPU or CPU ?
The level of speedup achieved over CPU execution reflects the suitability of the CPU to the application.
  Most applications have portions that can be much better executed on the CPU
  Some portions are easy to parallelize and so would benefit from being run on the GPU rather than the CPU

## Slide 24: GPU or CPU ?
GPU computations can be much more energy-efficient than CPU
  Simpler, e.g. No prediction, no cache, and slower clock
    e.g. http://www.nvidia.co.uk/object/gcr-energy-efficiency.html suggests basic operations can be 10x more efficient
    http://www.green500.org/sites/default/files/huang-hppac09-gpu.pdf - Just look at energy (forget Energy-Delay product)
  => lower power consumption / less heat
    REALLY important for large computers & data centres

## Slide 25: Other options and issues?
Other attached processor options
  E.g. DSP, FPGA
Many-core CPUs now also available as add-on compute devices
  E.g. Intel Xeon Phi, Many Integrated Core (MIC) architecture

## Slide 26: Other options and issues?
  E.g. Intel Xeon Phi, Many Integrated Core (MIC) architecture
    50+ Intel cores on a single chip, packaged as a PCI card, ~£2,500
    Each core supports 512 bits vector instructions, e.g. 16 single-precision operations at once (roughly like 16 SPEs)
    Roughly 1 TFLOPS (double precision), and able to run arbitrary code on each core

## Slide 27: Other options and issues?
Likely future convergence of GPU & CPU/multicore
  E.g. shared memory support
In general, energy efficiency is a HUGE issue today, not just performance

## Slide 28: Summary

## Slide 29: Summary
A GPU is an attached processor, specialised for operations common to 3D graphics
  Typically has several SIMD cores, each of which has many Stream Processing Elements (~ALUs)
    Can execute many floating point operations at once (highly data parallel)
  Has multiple memory areas with larger total bandwidth than main memory
  More cost and energy efficient than a general-purpose CPU

## Slide 30: Summary
Requires specialised programs:
  The general purpose host sends work items via command queues to kernels (functions) that run in many parallel threads on the GPU (device)
  (typically) no shared memory: requires memory movement to be programmed explicitly